## Slide 1: Projet FUI 01 janvier 2012- 30 avril 2016
pour des SImulations crédibles via la COrrélation calcul-essai et l’estimation d’incertitudes en DYNamique des structures
Project pilot : EDF R&D
Sylvie Audebert
Project duration | 40 months
Total cost | 3,82 M€
OSEO financial help | 1,45 M€
FEDER financial help | 68,9 k€

## Slide 2: Objectives and labellisation
Objectives:
  Quantification and improvement of the credibility of numerical models in structural dynamics thanks numerical-experimental correlation and estimation of uncertainties: demonstration on an industrial structure in complex environment
  Application fields: electricity production, petrol exploitation, transport and aeronautic industries
  Quantity of interest : modal characteristics
Labelled by:
  SYSTEMATIC
  Pôle Nucléaire Bourgogne
  Pôle des Microtechniques

## Slide 3: The 13 partners
Large companies | ASTRIUM EADS | EDF | NECS | SULZER Pumps France
Research institutes | CETIM |  |  | 
Intermediate size enterprises From 250 to 2000 persons | LMS-SAMTECH | SOPEMEA |  | 
Small and medium size enterprises <250 persons | PHIMECA Engineering | VIBRATEC |  | 
Universities | ENS Cachan | FEMTO-ST | INSA Lyon | MSME

## Slide 4: Principal demonstrator: Booster pump in industrial environment in EDF thermical plant
The Booster pump in SULZER Pumps France factory
The in situ non connected pump
The pump connected to
delivery and pipes
In situ
Modeled using finite elements

## Slide 5: Scientifical structuration

## Slide 6: Technological issues
  Apply current methods to complex and industrial large size structures
  Elaborate bolted built-up system models at macro-level
  Take into account the environment
  Influence of boundary conditions on the frequency response
  Perform the best compromise between fidelity of computational results to test data and robustness of numerical models regarding uncertainties

## Slide 7: Scientific innovations
1
Illustration of the complete procedure 1) modeling at macro-level, 2) a priori estimation of uncertainties, 3) measurement, 4) test-analysis correlation, 5) model credibility
2
Application of methods tested on academic examples on a complex structure in industrial environment
3
4
Observation of the total numerical variability by reproducing the real conditions of a study conducted by a design office (benchmarks)
5
Observation of the experimental variability on an in situ industrial system in situ (benchmarks)
Development and application of methods to quantify the total numerical uncertainty (parametrical + model form uncertainty)
6
Evaluation of the capacity of methods to quantify the total numerical uncertainty by comparison with the observed variability thanks to benchmarking operations
7
Determination of security coefficients and confidence intervals depending on problem classification

## Slide 8: SICODYN Benchmark Surrogate modeling
Karina Macocco & Felipe Aguirre
Phimeca Engineering

## Slide 9: Scientifical structuration
Part
1
State of the art
Part
2
Observation
of the
experimental variability
(benchmark)
Part
3
Observation
of the
total
num
e
rical variability
(benchmark)
Part
4
Test
-
analysis correlation
“best
compromise
” model
Part
6
Comparison of observed and
simulated numerical
variabilities
Classification
-
capitalisation
Part
5
Analysis of the numerical
variability via
confrontation
of
methods to quantify uncertainties
Benchmark data
base
Security
coefficients
Methods
Tool
box
12/06/2015 (F. Aguirre & K. Macocco)

## Slide 10: Study of the pump casing – variables & definition domain
Study of the pump casing – variables & definition domain
Uncertain parameters are the radius of the connecting screws of the frame with the other elements.
Uniform distributions
Radius type 1 [m] : [0,0088 ; 0,0132]
Radius type 2 [m] : [0,011088 ; 0,016632]
Radius type 3 [m] : [0,011088 ; 0,016632]
400 training points and 100 testing points
1h30 minutes per simulation with high RAM consumption (10 GB).
Total simulation time :
  25 days for the training points reduced to one day if distributed with Simulagora)
  6,25 days for the testing points (Distributed at Phimeca over 3 cores)
Notes: Meta-modele base d’apprentissage 400 points, base de test 100 utilise (plan de test) 6.25 sequentiel
2 jours Simulagora (20 machines) ou 2heures

## Slide 11: Input of the design of experiment
Sobol Sequence
  400 points for the training dataset.
LHS
  100 points for the testing dataset. Highlighted in the graph.
Notes: Quelles différences? Point gras point de test (signification)? R1 fixé => R2 et R3 aléatoire loi uniforme
Loi jointe R1/R2. Deux manières de constrution de plan d’expérience . Facilité d’enrichissement du plan

## Slide 12: Output of the design of experiment
Frequencies
Notes: Propagation des incertitudes. Quand uniforme? Linéaire?

## Slide 13: MAC matrix of the VGP
Notes: Métamodèle? Comparaison vis-à-vis du nominal les deux

## Slide 14: Adjustment graph of the VGP
Notes: Comparaison Méta-modèle modèle test 100 graphe d’ajustement.

## Slide 15: Validation of the VGP
Notes: Indicateurs?

## Slide 16: Validation of the VGP
Notes: Erreurs relatives, moyennes écart type et ? 7, 8 et 9. Points? (Verité – prédiction)/Vérité*100

## Slide 17: Perspectives
Bayesien